## Slide 1: Troubleshooting with QUIC
Alexandre Ferrieux, Isabelle Hamchaoui
Orange Innovation
In search of lost metrics

## Slide 2
  HTTP/3
  Standard Transport Layer
What is QUIC ?
  Child of the NSA scandal : Enhanced privacy, no linkability!
  A transport protocol similar to advanced TCP versions with deep encryption to avoid ossification
  30%of Orange traffic
  Start in 2014, IETF standard in 2021
QUIC

## Slide 3
Layer 4 in theory
End-to-end connectivity
TCP, UDP
Error control (TCP)
Flow control (TCP)
    The transport layer
Data
Ack
#6
#8
#9
#4
#2
Layer 4 TCP
Layer 3 IP
Layer 5+ HTTP
TCP
IP
HTTP
IP

## Slide 4
Reality check
Middleboxes interfere “illegitimately” in the Transport Layer Proxy, optimizer, etc.
Middleboxes far behind standards
 New Transport protocols blocked
 New TCP mechanisms blocked : e.g. TCP fast open
   Ossification of the Internet, innovation blocked for decades
    TCP transport layer
Data
Ack
#6
#8
#9
#4
#2
Layer 4 TCP
Layer 3 IP
Layer 5+ HTTP
TCP
IP
HTTP
IP
TCP

## Slide 5
  QUIC is an answer…
Data
Ack
#6
#8
#9
#4
#2
HTTP/2
TCP
TLS
IP
  TCP-like transport built over UDP + encryption
  Ossification-ender
  Middleboxes interference made difficult by QUIC headers encryption
HTTP/2
TCP
TLS
IP

## Slide 6
  QUIC is an answer…
Data
Ack
#6
#8
#9
#4
#2
HTTP/3
UDP
IP
QUIC
HTTP/2
TCP
TLS
IP
  TCP-like transport built over UDP + encryption
  Ossification-ender
  Middleboxes interference made difficult by QUIC headers encryption
HTTP/3
UDP
IP
QUIC
HTTP/2
TCP
TLS
IP

## Slide 7
  QUIC is an answer…
Data
Ack
#6
#8
#9
#4
#2
HTTP/3
UDP
IP
QUIC
HTTP/2
TCP
TLS
IP
  TCP-like transport built over UDP + encryption
  Ossification-ender
  Middleboxes interference made difficult by QUIC headers encryption
HTTP/3
UDP
IP
QUIC
HTTP/2
TCP
TLS
IP

## Slide 8
TCP one point passive measurement
Data
Ack
#8
#6
#8
#9
Losses
689
#4
#2
#8
421
TCP
  Upstream and downstream loss (+ delay) Location of the faulty segment / actor

## Slide 9
With QUIC, we’re not in Kansas anymore….
QUIC
?

## Slide 10
What else then? Packet drop counters?
    Poor and cumbersome diagnosis
    Counters not available in all nodes => no exhaustivity
    No upstream/downstream loss: where is the faulty segment / actor?
QUIC
    IP loss counters
?
?

## Slide 11
2-points measurements?
QUIC
?
?
?
?
?
?
?
?
QUIC
  No end-to-end degradation detection
  AP needs simultaneous captures from various (trusted?) actors
  Capture in customer OS?
    Access Provider lead
    Content Provider lead
  End-to-end degradation detection
  CP needs simultaneous captures from various (trusted?) actors
  Should we perform captures on behalf of Google? Facebook? Bullshit.com?

## Slide 12
Active measurement
QUIC
?
  Representativity (UE/server configuration, multipath)
   For specific investigations only
?
?

## Slide 13
Key disclosure
QUIC
  The dream solution!
  Key disclosure by client or server
  Awesome! Back to TCP debug
  Any chance to get it?

## Slide 14
The Loss bits mechanism
  What?
  Detect and locate faulty segments without packet number
  How?
  Reference patterns drawn in the packet flows with 2 bits in clear in the QUIC header

## Slide 15
The loss bits proposal (1)
Our proposal
Upstream Loss
Upstream Loss exposed via 1 bit in clear
N packets

## Slide 16
The loss bits proposal (2)
Upstream Loss
End-to-end Loss exposed via 1 bit in clear
Our proposal
End-to-end Loss

## Slide 17
The Loss Bits in the wild
Field Trial with Akamai in 4 Orange affiliates
    Akamai CDN servers with loss bits implementation
    Thousands of Orange real clients
    Loss bits mechanism refined and validated
    Additional validation by Satcom on Akamai servers and a satellite link
Core network
Internet
Acces network

## Slide 18
Wrap-up
    Current Troubleshooting practices are threatened
    In case of bad customer experience with QUIC, no easy way to locate faulty segment and prove actors’ responsibility
    New balance of power within the IETF arena
    Strong support from Akamai and CDN providers
    Very few operators expressed interest : Satcom, Telecom Italia
    Lukewarm support from Google, Microsoft, Apple
    Fierce opposition from Facebook and Mozilla
    Wait… Is loss still critical?
    BBR is quite robust to mild loss
    Other Loss sensitive services ?
    Our mechanism is ultra light, energy efficienty, and still useful for strong loss

## Slide 19
References
    First draft presented at IETF 104 (March 2019) https://datatracker.ietf.org/doc/draft-ferrieuxhamchaoui-quic-lossbits
    Orange-Akamai trial presented at IETF 105 (July 2019) https://datatracker.ietf.org/meeting/105/materials/slides-105-maprg-packet-loss-signaling-for-encrypted-protocols-01
    Akamai+lightspeed step-in at IETF 106 (November 2019) https://datatracker.ietf.org/doc/draft-ferrieuxhamchaoui-tsvwg-lossbits/
    Satcom trial presented at IETF 106 (November 2019) https://datatracker.ietf.org/meeting/106/materials/slides-106-maprg-losses-in-satcom-systems-identification-and-impact
    Joint draft with Telecom Italia (mars 2020) https://datatracker.ietf.org/doc/draft-mdt-ippm-explicit-flow-measurements/
    Independent evaluation from Ike Kunze et al. (Aachen university)
    L, Q, R, and T: which spin bit cousin is here to stay? (ANRW '21)

## Slide 20: Thank you